## Slide 1: Octane’22 Review Presentation
Project : Pad printing defect inspection system using Vision
Department : MTD R&A (Engineering)
Mentor : Pravin Marathe

## Slide 2: Pad Printing
Pad printing is a printing process that can transfer a 2-D image onto a 3-D object.
Pad printing is used in automotive industry.
Indicator parts, Dashboard components, Wheels etc.

## Slide 3: Pad Printing
Dataset collected from Vendor visit to BLG Logistics
Date: 13-06-2022

## Slide 4: Possible defects
What are the possible defects in pad printing?
    Print cut
    Print shift
    Partial print
    Double print
    Print edge burr
    Print smudging

## Slide 5: Possible defects
Smudge
Print Smudge

## Slide 6: Possible defects
Print Cut
Cut at P
Cut at logo

## Slide 7: Possible defects
Smudge
Dust
Print Cut

## Slide 8: Probability of defects
(a) LH
(b)RH

## Slide 9: Machine Vision Inspection System
Vision inspection systems provide image-based inspection automated for your convenience for a variety of industrial and manufacturing applications.
2D machine vision system is used.
Major components : Lighting, lens, image sensor.
Benefits:
  Lowers Costs
  Eliminates Human Error
  Identifies Print Defects
  Low inference time
  Reliability
  Simple Layout

## Slide 10: Vision system Camera
For identifying defects using OpenCV, camera used can be of low resolution
For identifying defects using deep learning, camera of high resolution should be used.
Bassler acA2500-14uc
Sensor : MT9P031
Shutter : Rolling Shutter
Sensor Type: CMOS
Sensor Size : 5.7 mm x 4.3 mm
Resolution : 5 MP
Frame Rate : 14 fps
Logitech C270
Sensor Type : CMOS
Resolution : 720p
Frame rate : 30 fps

## Slide 11: Approach towards identifying defects
Print shift
Print Cut
Double print
OpenCV
Partial print
Print smudging
Print edge burr
Other defects like scratches, dust etc
Deep Learning

## Slide 12: Image Pre-processing
Image
Thresholding
Edge detection
Masked image
Bitwise operation
Morphological Transformation
To improve the quality of the image so that we can analyze it in a better way.
Programming Language used: Python
Libraries used : OpenCV, NumPy, matplotlib

## Slide 13: Deep Neural Networks
Why deep learning over machine learning?
  Differ in how each algorithm learns and how much data each type of algorithm uses.
  Deep learning automates much of the feature extraction piece of the process.
Neural Networks
  If the output of any individual node
  is above the specified threshold value,
  that node is activated, sending data to
  the next layer of the network.

## Slide 14: Transfer learning
Storing knowledge gained while solving one problem and applying it to a different but related problem.
Advantages:
  Saves time and resources
  Improves efficiency
  Provides generalised way

## Slide 15: GPU vs CPU
Pros
Cons
Requires less memory
Faster
Parallel instruction processing
High throughput
Google colab allows to connect to local runtime using Jupyter.
Deep Learning uses a lot of processing power.
Weak cores
Less diverse
Serial instruction processing
Low latency

## Slide 16: ResNet vs MobileNet-V2
Resnet
Mobilenet V2
Resnet
Identity shortcut connection
MobileNet-V2
Less no. of parameters

## Slide 17: Loss function
Epochs
Epochs
Loss
Loss
ResNet
MobileNet-V2
Decreasing loss function as preferred.
Quantifies the difference between the expected outcome and the outcome produced by the model.
Backpropagation

## Slide 18: Data Augmentation
When there is limited data we increase our data set by performing some actions.
Flip
Rotation
Scale
Crop
Translation

## Slide 19: Model identification
Available models:
Svartpilen spoke black
Svartpilen alloy
Vitpilen spoke grey
Vitpilen alloy

## Slide 20: Output – Smudge defect

## Slide 21: Output – Smudge defect

## Slide 22: Output – Smudge defect

## Slide 23: Key benefits
Wheel undergoes 3 stages of screening.
With this model, this will be reduced to one stage.
Algorithm-1
Model Identification
Algorithm-2
Identification of defects

## Slide 24: Future work
Edge computing solutions
  Jetson Nano
  Eliminates trade off between speed, performance
  Cost effective
Diversity among data
Optimization of parameters

## Slide 25: References
Detecto documentation
Neural networks

## Slide 26: Thank You!